## Slide 1: PI WebAPI Introduction
Jesse Ru, Customer Support Engineer
jru@osisoft.com
March 23, 2016

## Slide 2: About OSIsoft

## Slide 3
We believe People with Data can Transform their world

## Slide 4: OSIsoft is Truly a Global Company
São Paulo, Brazil
Perth, Australia
Singapore
Shanghai, China
Frankfurt, Germany
Seoul, South Korea
Manama, Bahrain
San Leandro, CA
Houston & Longview, TX
Montreal, Quebec
Philadelphia, PA
Mayfield Heights, OH
Calgary, Alberta
Madrid, Spain
Moscow, Russia
Ostrava, Czech Republic
Beijing, China
Mexico City, Mexico
Phoenix, AZ
Johnson City, TN
Savannah, GA
Paris, France
Durban, South Africa
Sydney, Australia
Tokyo, Japan
London, UK
OSIsoft Offices
OSIsoft Headquarters

## Slide 5: A Unique and Proven Vision
For over 30 years OSIsoft has:
Infrastructure for consolidation and centralization of sensor based data
Open infrastructure to support best of breed ecosystems
Scalability from small deployments to enterprise deployments
Infrastructure for change
Infrastructure for empowering people

## Slide 6
400+
Pulp & Paper
sites deployed worldwide
91%
100%
of the Global Fortune Top 10 Metals & Mining companies
37 of 50
of the World’s Largest Chemical & Petro- Chemical
companies
9 / 10
of the Global Fortune Top 10 Pharma
companies
Over
1,000
of the world’s leading
Power & Utilities companies
95%
of the Global Fortune Top 40
Oil & Gas companies
OSIsoft is trusted by the world’s leading companies

## Slide 7
Over the past 12 years, over One Thousand customers have spoken about the Power of what OSIsoft has done for their business
Hear our customers speak
1,015

## Slide 8: What we build

## Slide 9
  Rolled-up quality data for
  supervisors
Creating islands of systems
Demanding we connect data, to systems, to people, to actions
Availability and accessibility of this data is critical
Real-time Operations Data is being created everywhere

## Slide 10: Silos to Standards / Complexity to Simplicity
SCADA 1
LIMS
CBM
Instrument
ERP
Asset Reliability
PLC2
PLC1
DCS 1
DCS 2
CAPA
Instrument
SCADA 2
Controller
EMS
Learning Mgmt.
Planning and Scheduling
Traditional Strategy
PAT 1
PAT 2
Historian
Excel
Notes: Intention of this Slide:
The audience gets how the ‘traditional’ strategy is unworkable.
They identify this slide with their own data situation.
Narration:
Let's start with just the big picture of the PI System - what is this whole thing called the PI System and what does it actually provide. Now let's start with where a lot of our customers find themselves before they use the PI System.
If I stripped it all down it really starts with you have people that have some tasks that need to get done (here on the right), and you have sources of data that those people want to have access to and need to have access to (here on the left). There’s SCADA systems and there's instruments and there's plant control systems and all that is data that these people need. Usually what our customers have before the PI System looks a bit like this.
[first animation]
There's a whole variety of places that they store data: there's an Asset Reliability system, there is a condition based maintenance system, there's a learning management system, and there is a historian for some of the data - and all the systems play different important roles.
[Second animation]
And often our customers start linking these up! The SCADA system feeding to the historian, and other systems feeding their data the historian, and then the Asset Reliability system gets some of its data from the historian BUT it also needs some really specific data from the SCADA system that got washed out in the historizing process… so it needs to be connected directly to the SCADA system. Meanwhile the Condition Based Maintenance [CBM] system is getting data from the historian but also needs specialized asset information from one of the data sources.
[Third animation]
Then that data needs to be forwarded to Excel, and the Planning and Scheduling System and then on to all the people they need to use it. Maybe you hire a whole integration team to tie them together, or maybe you just spent hours each week formatting the data and copy and pasting it in just to send of a spreadsheet that goes stale the moment you email it.
And this is the traditional strategy. One of our customers in Europe actually referred to this as the ‘spaghetti’ strategy they found themselves in.
Additional Notes:
I encourage you to replace the acronyms on this slide with what you know this customer has.
Some of the default: acronyms
DCS – Distributed Control System
CBM – Condition Based Maintenance
LIMS – Laboratory Information System
ERP – Enterprise Resource Planning
PLC- Programmable logic controller
SCADA- Supervisory control and data aquisition
You can bring out the challenges of data collection (variety of formats, geographically spread, speed, breath). The challenges of managing the data (spinning up new databases & silos, storing only averages, slow response times, months to build a new project), and visualizing the data & making the data valuable (copy & paste, email, wait times to retrieve data, needing to code, wait for custom code, then manage it ongoingly)
---------------------------------

## Slide 11
in·fra·struc·ture [in-fruh-struhk-cher]
“It can be generally defined as the set of interconnected structural elements that provide framework supporting an entire structure of development1”
1 Online. January 7th 2014. http://en.wikipedia.org/wiki/Infrastructure
Traits of an Infrastructure
Reliability
Availability
Scalability
Extensibility
Agility
Connectivity
Security
Simplicity
What is an Infrastructure?

## Slide 12: Silos to Standards / Complexity to Simplicity
SCADA 1
Instrument
PLC2
PLC1
IPC 1
IPC 2
Instrument
SCADA 2
Controllers
PAT 1
PAT 2
LIMS
ERP
Asset Reliability
Learning Mgmt.
Collect
Enhance
Deliver
Notes: Intention of this Slide:
The audience has the experience of resolution after the tension and messiness of the previous slide.
The audience gets that implementing a data infrastructure like this is attractive and a no-brainer
Narration (editing not finished):
Here's what that world looks like after a customer implements the PI System.
You start with all the same people, and all the same sources of data, and all those people have all the same tasks they need to get done.
[First animation]
Now imagine we could have a single layer that was responsible for collecting all of the data from any of those sources, in the highest fidelity possible.
[Second animation]
That layer passes that data onto a second layer that's responsible for storing the data, and doing first pass enhancement on it (like noticing events and running real-time calculations).
And then that layer passes it on to a third layer
[Third animation]
…that's responsible for delivering the data. Both delivering it directly to people that will do something with it, or delivering it to other systems. The PI System doesn't do everything, and many of the specialized systems that you had before will still exist, but imagine that if instead of needing to string them all together to pass data back and forth you can have one system that was responsible for collecting and delivering that data to those systems. And then those systems can send their data onto the places and people it needs to go to.
The PI System’s central strength is that it can collect timeseries data from any source, store it in its highest fidelity possible, and simultaneously deliver real-time data to any person or other system that needs to get it.

## Slide 13
PI Interfaces
PI Server
PI Tools
Collect
Manage
Enhance
Deliver
The PI System has 3 Layers
Notes: Intention of the Slide:
To set up the ‘agenda’ of the following slides
The audience gets that even though the various PI products the speaker is about to cover have distinct responsibilities, they all operate as part of one system.
Narration:
Okay so now will get into the individual pieces of the PI System - the individual pieces of software that have names that you might've heard like ‘PI Server’ or ‘PI Coresight’.
The three layers I mentioned: there is a layer that collects information, there's a layer that manages that information, stores and enhances it, and there's an layer that is responsible for delivering that information.
Any of our products falls into one of these three categories - and they all are part of one system and they all work together

## Slide 14: Pervasive Connectivity PI Interfaces
PI Interfaces
Manual
SCADA
PLC
Databases
Sensors
Directly connects to more data sources than any other operational data collection system
DCS
Notes: Intention of this slide
Leave the audience trusting the PI System can connect to THEIR operational data,
The audience values choosing a software vendor that has no preference for what data is brought in (like OSIsoft)
Why?
We’ve been at it for over thirty years (thus we have a long library of interfaces, including old technologies no one would write new interfaces for today)
We’re agnostic (We are enthusiastic about reading ANY data you use. we have no preferences for what data you bring in, unlike historians that come with control systems)
We’re global-sized (We are big enough to support the engineering group required to develop and support this many interfaces)
Narration:
(start with referencing the homework you did) So in talking to you earlier I asked what source of data you connect with, and how you connect with X and Y systems.
One of the main strengths of the PI System is that it connects to any source of data out there – and it's built to natively read from over 300 industrial automation standards and systems.
  (note: we’re using the 300 figure here to align with the number of active interfaces we have. 450+ is often quoted, that number refers to the total number of interfaces OSIsoft has ever written. Some of those are inactive)
Often our customers have one control system and maybe a secondary control system somewhere else, then a different plant or simply some data that they have to manually get to that is in a difficult to get to takes a lot of time.
[first animation]
What if you could take all the data and automatically pull it into one system? Even if that equipment was installed decades ago, or you still needed to manually record it, it could immediately go into that one system. Then looked at side-by-side with all the other data without having to deal with going over here to this system to get data, then going over here to that system to get data? Data set is all in one place. OSIsoft produces a whole family of ‘PI Interfaces’ as we call them: a PI Interface is a piece of software that connects to a specific source of data. This could be a control system, it could be a certain industrial automation standard, it could be another type of historian for data! We've written interfaces to connect to many, many, many of them so whatever data you have out there can be put into the PI System.
In the end the PI System and provides pervasive conductivity. Like how the roots of the tree can pervasively go through the ground and get everywhere, the roots of the PI System can reach to any source of data and get it back to the PI System.
Notes to the account manager:
What you say is really going to be customized to the type of data that this customer is dealing with. Interfaces can take data that is a slow drip, all the way up to performance that is needed to monitor the stability of the electric grid. That’s 60 reads a sec – over a wide distributed geography. Most customers never will use that – yet it gives you a sense of the quality of these interfaces.
Some customers are really concerned with the rate at which data can be read - maybe phasor data or some other really high rate data – and they're concerned if your system can keep up with it. In that case, during the section you should highlight the performance of our interfaces. That they can really take high speed data.
Some customers are concerned that can you collect the number of data streams that I need to consume? In which case, highlight that we have interfaces that collect data for utility customers that span over wide geographies with millions of data points coming in nonstop.
Or maybe this customer has just one source of data, coming at a moderate speed. In which case maybe want to highlight that ‘we have you covered on that one source - and when you get new source of data in the future, you can trust the PI System will bring it in without an expensive custom integration project.

## Slide 15: Proven Engine PI Server
© Copyright 2015 OSIsoft, LLC
Common PI Server
~20 M writes/day
Big Data Cluster
100+ machines
9 B writes/day
High Performance PI Server
43 B writes/day
A PI Server is:
System of Record
Real-time Processing
Data Calculations
Alerting Engine
Metadata Layer
Event Tagging
PI Server
Notes: Intention of this slide
Leave the audience with no question in their mind that the PI System’s raw performance is top of class. We are very strong in any performance comparison.
The audience believes the PI Server’s performance is appropriate for their needs (big or small)
Narration:
The anchor, and the longest-serving piece of the PI System is the PI Server. This is the piece of software that's responsible for taking in all the data coming from those interfaces, storing it forever, and storing it at the highest fidelity possible. All the while allowing access to historical data very quickly due to the way that we structured the database to be optimized for time-based data.
One aspect of the PI System and the PI Server that you want to understand is that we are optimized for time-based data. A lot of business systems and accounting systems are relational systems – optimized for tables of data. The PI System is dealing with sensor data that's coming in nonstop, and might be coming in at different rates… maybe those sensors over there are being held up and then coming in all at once. It's a massive performance challenge for a server, and the reason the PI Server is particularly good at this task is it is designed from the ground up as a time-based system.
The PI Server scales from small to very large and performs well at all these levels. Now to give you a sense of that, let me start here.
[first circle animation]
This circle represents a typical PI Server that many of our customers might initially have. Say you have 500 data streams - we call them tags - 500 tags, and each tag is reporting maybe 30 times a minute. Overall, that’s something like 250 events per second, or 15,000 event per minute for the server to handle.
[second circle animation]
There's a big data cluster that was up publicized by eBay in a talk around a year ago that I find represents what a high-performing big data cluster can do. It had around 9 billion rights per day. That’s a lot of Data! And that's what this circle represents. The cluster was a hundred (plus) machines working in concert to handle this amount of data. Relational big data systems like this and time-based data systems like PI are different animals, but this gives you a sense of how fast computers are going these days. If we compare that back to our typical initial PI System, using a back of the envelope calculation to scale that up to a day, hat turns out to be around 21M events per day coming in.
Now we say that the PI Server scales very well to really high levels. So we put the PI Server software and a top-of-the-line piece of hardware and tuned it all up like a racecar to see how fast we could actually take it out. We found that we could make a single machine operate at Five Hundred Thousand writes per second. That's per second. If we take up to ‘per day’ that's 43 billion rights in a day.
[third circle animation]
Now many of our customers are never to be using that volume of data. But we want you to know that the performance of the PI Server can grow with you to any size you will ever get to. And we’re laser focused on the software we make and will continue to develop on the PI Server for years and years to come.
(optional)
Look back 5 years. Or 3 years even. Did you know you’d be using the data you’re using today? Worldwide Data Use is growing. FAST. If you look at a rate of data growth in the world its clearly doing this <gesture exponential curve>. With PI you have a secure future and you know you won’t hit the limits of your PI System in two years. Or ever. We are constantly working on expanding this circle so YOU don’t have to work at expanding it. That’s what we mean by Future-proof.
[pause – questions, or just to shift topic]
But this is all just numbers of writes per day which is just one kind of measurement and usually out of context from all the actual tasks you need your data infrastructure to do. That PI Server in that circle has many capabilities.
It's of course a system of record in historizing all that data. And it excels at that task. And it also delivers real-time data for any data stream. So it historizes AND delivers real-time streaming data simultaneously. That's a big differentiator for the PI System. Now, inside the PI Server, real-time calculations can be run on the data as it's coming in. And alerts can be sent out via text or email. And there's a major metadata layer that adds context onto all of this data to help you and the other humans sort through your hundreds or thousands or millions of data streams. I'll talk more about that later. All that happens inside one of these circles.
The Math on this Slide:
‘Typical’ Initial PI Server
Write rate = 250writes/sec. (500 tags * 30 events/min just a back of the envelope calculation, this is not based on any specific customer)
If 250/writes/sec correlates to 0.08in^2
If Area = 0.02in^2, Diameter = 0.16in
Ebay-Cassandra Big Data Cluster
Write rate = ‘>9 billion writes/day’ (104k writes/sec)
If Area = 8.66in^2, Diameter = 3.32in
Source: Slide 16 of https://onedrive.live.com/redir?resid=E9063DDBD0D51694!1291&authkey=!AOhVwP88QDkM7Og&ithint=file%2c.pptx
High Performance PI Server
Write rate= 500,000 events/sec (write performance of Denis’ 20M point PI Server running on a single Dell PowerEdge)
If Area = 41.62in^2, Diameter = 7.28in
Notes to Speaker:
Do not diminish the big data cluster achievement – 9 billion a day is impressive – besides, the better it looks, the better the PI System will look
References:
The cluster size needed to achieve parity in terms of performance for a high-end PI server can be quite large. Organizations like eBay and Netflix stand up along the lines of 100+ servers to get the write performance of Denis’ 20M point PI Server running on a single Dell PowerEdge. Datastax’s own slides that I captured from last year’s Big Data TechCon shows clusters sizes of 12 servers to get to 80K writes/sec (VLDB benchmark) and 32 servers to get to 35K writes/sec (Endpoint benchmark). Netflix reported needed roughly 300 servers to do 1M writes/sec.
See slides 14, 15, and 21 of my Primer presentation: https://onedrive.live.com/redir?resid=E9063DDBD0D51694!1291&authkey=!AOhVwP88QDkM7Og&ithint=file%2c.pptx

## Slide 16
Fit your users PI Visualization Tools
PI DataLink
Access data from Excel
PI ProcessBook Visualize process in real time
PI Coresight
Anywhere, Anytime
PI Tools
Notes: Intention of this Slide:
The audience connects the power of having visualization tools be able to show any of their data
The audience is satisfied that native out-of-the box PI System visualization tools will fit their fundamental needs (spreadsheets, mobile, web, & process displays)
Note:
This slide is titled ‘PI Visualization Tools’, and highlights the client products that will apply to only the broadest set of customers. You may have heard ‘PI Visualization Suite’ (PVS) as well. PVS is a defined PI Client package that OSIsoft sells. It includes some client products that would only be used by specific customers. Pi Visualization Suite includes:
PI Visualization Suite-
  PI Coresight
  PI DataLink
  PI Manual Logger*
  PI Manual Logger Mobile*
  PI ProcessBook
  PI WebParts (includes PI DataLink Server)
  PI BatchView
  PI ActiveView
Narration:
So we've covered the collection layer, and what the PI Server can do, now let's get a look at the layer which delivers data. Now all that server power and capabilities and calculations are only as good as people being able to see them. OSIsoft produces a set of visualization tools that are natively integrated with the PI System to do fundamental time based data jobs really well.
One thing that we know engineers use lots of the spreadsheets so we have. And if you're an engineer who has data you want put it likeSo we've covered the collection layer and some of what the PI Server can do in the inside now let's look at that last layer delivery.
OSI soft itself has directly created and published and maintains a set of visualization tools that are natively integrated with all the PI System capabilities.
First off there's PI Datalink. If you've ever worked with spreadsheet, if you're an engineer and you have data and you work with Excel, you want PI Datalink. If you've ever found yourself copying and pasting data between sheets or emailing around data…. PI Datalink and help you out. Imagine having a query to the server and changing one cell to ask for another day’s worth of data - and suddenly poof all the data just appears in your spreadsheet. PI Datalink does that plus you can leverage all of the functions that are natively in Microsoft Excel. We’ve even added a couple functions. Since timeseries data doesn't regularly appear in Excel we built specialized functions that work very well with it.
Next you may a visual dashboard of your data, maybe a clone of an HMI (Human Machine Interface) screens or process screens your operators are looking at. Wouldn’t it be useful to see what they are seeing? PI ProcessBook is a tool that allows you to build any display that you want and have real-time data streaming into it. You can build PI ProcessBook screens that look exactly like operator control screens but are only read-only. And any display can show real-time updates or any historical data. In other words, Rewindable and Playback-able displays. What if you could see exactly what operators are seeing from outside the control room - that's a PI ProcessBook really allows
And many of our customers now have the need to see their data on mobile devices or on the web. PI Coresight takes data and puts it into displays you can throw together with a number of clicks and drops. You can combine any data in the PI System into a quick display, or show any of the PI ProcessBook screens you've made over the web using PI Coresight. It's specifically built to be an intuitive quick tool that you can use. And there PI Coresight formats designed for phones, tablet computers and desktop browsers.
Notes to Account manager:
This slide should be tailored to what this customer is interested in. The narration above is generic and will be more powerful if you bring in their concerns
Other points to bring in at your discretion:
Future releases. No custom code to maintain
Performance. Native link to PI Data Server
Speed. Server side work makes comparison of huge manual sheet (before) vs PI DataLink sheet (now)
International, and ready to go the moment of purchase no waiting on a custom build
Proven software.
Visualization tools native to your whole data infrastructure. No custom integration needed
Stitching together solutions is expensive. No custom code to re-integrate
New NERC CIP regulations next year? We ensure your tools pass regulations now and the future
PI DataLink – Excel
Right Now’s operational data
Last year’s data in an instant
The PI Server can get data in and get data out really fast – which MATTERS when you want to run an Excel report or be checking up on the real-time status of a line. (Ask the customer users what gripes they run into).
History and Real time (yes PI Datalink can receive updates every few seconds)
Manage Spreadsheet forking (by hosting the calculations on the PI Server, the spreadsheet is housing fewer forkable calculations)
Data in any spacing. No custom code to create and maintain
PI ProcessBook - Displays
See what’s happening Now
Rewind a control room display
What if you could see data, the way the operators in the control room see data? The PI System gets data out of the control-room securely because its one-way – we don’t write back – and PI ProcessBook allows you to create data dashboards similar to anything you’ve encountered in the control room. AND what’s more, you get to use all the real-time AND history the PI System offers.
HMI displays, natively integrated with the PI Data Server
‘I want to see what the operators are seeing’
‘I want to see what the operators saw’
Rewindable and playback-able display
PI Coresight
Mobility. Show HMI displays anywhere with PI Coresight
Second, we made sure that your vehicles can move faster on the highway. This is true whether you’re driving cars, pickups, semis, or even wide loads.
The analogy here is that you might have casual users, heavy users, and some data-intensive applications like BI or analytics. In all cases, your applications run much faster with PI Server 2012 so users do not have to wait. For example, think of a large end of the month report using PI DataLink in Excel. This would be a big hit on the PI Server and may impact performance for operators. PI Server 2012 allows users to run these reports without affecting normal operations.
Again, when you want to upgrade a system, these already work with each other.

## Slide 17
Partner Applications
PI Integrators
Move data between business and geographic boundaries.
PI Data Access
Programmatic access to build anything on PI
Boundless Open data export
</>
PI Tools
Notes: Intention of this Slide:
The audience gets that the applications of the PI System are endless and customizable. Anything system the use can draw data from the PI System
Narration:
One of the greatest challenges coming up for companies in this era is moving data (lots of data) across business and geographic boundaries
As I said before one of the big aspects of the PI System is that it's an open infrastructure: we read from just about any operational data source out there.
But also important is where the data goes after the PI System. There's a lot of other systems out there to do amazing things. Things like mapping software, or big data analytics. Things that the PI Server isn't designed to do. We're interested in being a data infrastructure that makes life easy for all of those specialized applications.
In that interest we've built a number of exporting options. Things like PI Integrators - these are pieces of software that are designed for another vendor’s specific software. Or PI Data Access - that's a set of programming libraries that you can use, or an integration partner of ours can use, to build a specific custom application for you using the data that's in your PI System data infrastructure. There’s a whole library of partner-produced software specific to individual industries and applications.
We maintain partner agreements with many companies, both small shops that integrate PI System software to large global organizations. These alliances allow us to play well with any other system you have or specific need you bring.
Integrator types: BI, Big Data, Predictive Analytics, Business System, and Geographic

## Slide 18: The PI System Infrastructure
PI Data Archive
PI AF
Machine Friendly :]
Human Friendly :)
‘The pump is down - what’s happening?’
PI Coresight
PI ProcessBook
PI DataLink
PI Notifications
OPC
Modbus
Databases
Text Files
PI Server
ACTUATORS
MOTORS
PUMPS
Notes: Here’s where we introduce data flow in the PI system at a deeper level. This builds up from a single example of using PI Coresight to access OPC data on a pump, to a full blown infrastructure. It’s here in place of our old data flow diagrams. Different courses will get into the nitty-gritty of data flow, but this slide gives a broad overview and labels right from the start that the PI Data Archive tags are “machine friendly” and PI AF elements or attributes are “human friendly”. PI tags are the old way of finding data, AF is the new and improved way.
EXAMPLE: Here’s an example. Again, we have a data source, in this case a Pump. We also have a user – on the right. That’s you. You notice the pump has failed and you want to know what’s happening. We’re going take a look at how the data gets from the Pump, through the PI System Data Infrastructure and on to you so you can investigate the issue.
<click> Essentially, the PI system is like a translator.
<click> It can speak both a machine friendly language, <click> and a human friendly language. <click> The machine friendly language the PI System will speak in this case is OPC. This is a common protocol that a lot of instrumentation exposes its data. In this case we’re reading from a pump. The interface will constantly read the flow rate, bearing temperature, and what state the pump is in. <click> This data is constantly sent to the PI Server. <click> more accurately, this data is sent to the PI Data Archive, one of the components of the PI Server. All the readings I spoke of make up what we call PI Tags. Each one – flow rate, temperature and state are different tags in the PI Data Archive. Whenever the interface gets updated flows, temperatures or states for the pump, this is sent through and stored in these tags. Now, the PI Data Archive still sits on the “Machine Friendly” side of the fence here. <click> On the human friendly side, we have PI AF. PI AF provides an organised view of PI Data, and can also reference other sources. Say that you want to find out when the last time this pump was maintained? PI AF grabs that from a maintenance database somewhere else in the company, and shows it to you right alongside the current production data, in the same dashboard. <click> The final piece of the puzzle in this scenario is PI Coresight. This is one of the tools that we’ll be studying in this course. You visualize the data using PI Coresight and look at the pump’s performance over the past few months. You find that since the last time the pump was maintained, its efficiency isn’t where it should have been and it’s finally failed. Someone’s going to be in trouble. <click> This might be all well and good, but your organisation has many different systems <click> and many different users that need data from these systems. <click> The PI System can read asset data from all the equipment in your facility, using any standard or protocol it supports, <click> and help people in your organisation do their jobs by delivering that asset data to them in a standard way. During this course, we’re going to study how you can use many of these user applications to take full advantage of the PI System.

## Slide 19
Immediate Value
Accessibility of information
Collect data from Disparate sources
Connect information to people
Speed to deployment
Value over time
Operations Management
Quality Management
Equip. Health Management
Performance Management
Infrastructure Value Over Time
Asset/Process
Intelligence
Operational
Intelligence
Business Intelligence
Engineers
Plant / Operations
Managers
Operations
Leaders
What:
To Who:

## Slide 20
Quality
Safety & Security
Energy
Utilization
Process
Efficiency
Regulatory
Performance
Asset Health
Process Engineers
Production Superintendents
CoE experts
Location Managers
Regional/Global Ops
Business leadership
Operators
Craftsmen
Supervisors
An Infrastructure helps data drive results across the enterprise
Achieve daily targets
Resolve immediate issues
Maintain schedule/plan
Safe operations
Detect excursions
Maintain process stability
Improve productivity
Improve quality
Understand/grade perf.
Adjust expectations
Establish plans
Calculate forecasts

## Slide 21: What if you could leverage your data assets to…
Key Performance Indicators
Centers of Excellence
Real time action
Best practices
Continuous innovation
Energy rates
Raw material costs, raw
material quality
Water rates
Labor rates
Environmental regulation / mandates
Process productivity
Product quality / genealogy tracking
Critical asset life / maintenance costs
Energy / raw material / natural resource consumption
Environmental performance / regulatory compliance and reporting
1
Enterprise Visibility and Management
2
Awareness
& Impact of Uncontrollable Factors
3
Directly Impact Controllable Costs / Performance

## Slide 22
Quality
Safety & Security
Energy
Utilization
Process
Efficiency
Regulatory
Performance
Asset Health
$300k in savings Water temperature permit compliance
Recovered 640M liters of treated water
Reduced 5 unplanned shutdowns in 2013
Reduced facilities energy costs by over $2M
Avoided up to $2M savings if unit failed
Over $2.8M in savings from event prevention
Business Impacts: An agent for change

## Slide 23: How Data is Stored

## Slide 24: What is a PI Data Archive Tag (Point)?
A unique storage point for data in the PI Data Archive. Simply a single point of measurement.
Data Source
PI Interface
PI Data Archive
Static Data
Relational Database
PI AF Server
PI Visualization
Suite
Notes: Time stamp and value are stored in the archives.

## Slide 25: Useful PI Tag (Point) Attributes
Tag Name
  Unique name of the tag
Descriptor
  Tag’s description
Pointsource
  Allows grouping of tags for a better organization
Zero and Span
  Define the minimum and maximum values.
EngUnits
  Engineering units (units of measure).
M03_E1P1_MOTDRV1202_RUNSTAT
Machine3 Encloser 1 panel 1 Motor Drive 1202 Run Status
Notes: Example of a tag name. It means: Machine3 Enclosure 1 Panel 1 Motor Drive 1202 Run Status
Zero and Span: These define the minimum and maximum values and are used in a number of places. Most obvious are the upper and lower
boundaries of object like the trend, bar graph, or multistate symbol.

## Slide 26: The PI System Infrastructure
PI Data Archive
PI AF
Machine Friendly :]
Human Friendly :)
‘The pump is down - what’s happening?’
PI Coresight
PI ProcessBook
PI DataLink
PI Notifications
OPC
Modbus
Databases
Text Files
PI Server
ACTUATORS
MOTORS
PUMPS
Notes: Here’s where we introduce data flow in the PI system at a deeper level. This builds up from a single example of using PI Coresight to access OPC data on a pump, to a full blown infrastructure. It’s here in place of our old data flow diagrams. Different courses will get into the nitty-gritty of data flow, but this slide gives a broad overview and labels right from the start that the PI Data Archive tags are “machine friendly” and PI AF elements or attributes are “human friendly”. PI tags are the old way of finding data, AF is the new and improved way.
EXAMPLE: Here’s an example. Again, we have a data source, in this case a Pump. We also have a user – on the right. That’s you. You notice the pump has failed and you want to know what’s happening. We’re going take a look at how the data gets from the Pump, through the PI System Data Infrastructure and on to you so you can investigate the issue.
<click> Essentially, the PI system is like a translator.
<click> It can speak both a machine friendly language, <click> and a human friendly language. <click> The machine friendly language the PI System will speak in this case is OPC. This is a common protocol that a lot of instrumentation exposes its data. In this case we’re reading from a pump. The interface will constantly read the flow rate, bearing temperature, and what state the pump is in. <click> This data is constantly sent to the PI Server. <click> more accurately, this data is sent to the PI Data Archive, one of the components of the PI Server. All the readings I spoke of make up what we call PI Tags. Each one – flow rate, temperature and state are different tags in the PI Data Archive. Whenever the interface gets updated flows, temperatures or states for the pump, this is sent through and stored in these tags. Now, the PI Data Archive still sits on the “Machine Friendly” side of the fence here. <click> On the human friendly side, we have PI AF. PI AF provides an organised view of PI Data, and can also reference other sources. Say that you want to find out when the last time this pump was maintained? PI AF grabs that from a maintenance database somewhere else in the company, and shows it to you right alongside the current production data, in the same dashboard. <click> The final piece of the puzzle in this scenario is PI Coresight. This is one of the tools that we’ll be studying in this course. You visualize the data using PI Coresight and look at the pump’s performance over the past few months. You find that since the last time the pump was maintained, its efficiency isn’t where it should have been and it’s finally failed. Someone’s going to be in trouble. <click> This might be all well and good, but your organisation has many different systems <click> and many different users that need data from these systems. <click> The PI System can read asset data from all the equipment in your facility, using any standard or protocol it supports, <click> and help people in your organisation do their jobs by delivering that asset data to them in a standard way. During this course, we’re going to study how you can use many of these user applications to take full advantage of the PI System.

## Slide 27: What is an Asset?
An asset represents a logical or physical component of a process.
Data Source
PI Interface
PI Data Archive
Static Data
Relational Database
PI AF Server
PI Visualization
Suite

## Slide 28: What is an Asset (element)?
Tanks
Heat Exchanger
Boilers
An asset represents a logical or physical component of a process.
PI AF Server

## Slide 29: What is an Attribute?
An attribute represents a unique property associated with an asset.
  Based on individual points, calculations, static object specifications, etc.
Notes: As an example, if I want to find TankA’s the level or Volume; I just need to browse the tree structure and then I will be able to find the information I was looking for.
What is an attribute:
Attributes represent a unique property associated with an asset.
The attribute maybe a constant, a value from an internal PI AF table, a value from an external database or a storage point for data in the PI Data Archive.

## Slide 30: Filtering Noise (Exception Test)
Last reported value
This value falls outside the deadband, so the interface reports it to PI, along with the Previous value
Notes: Stored values:
The first Value
The one that falls out
The one right BEFORE the one that falls out

## Slide 31: Exception Test
When a value passes this test, that value and the previous value are reported.
  Why? To have a better representation of the actual tag behavior.
Snapshot value
+/- ExcDev
Trend if previous value is not sent
Previous value
Trend if previous value is sent
Temperature
Time
passes the exception test

## Slide 32: Raw Data - Example
Raw values scanned on the data source.
  Without Exception and Compression tests, these would all be archived.
Time
Temperature

## Slide 33: Exception Test - Example
P
E
P
P
P
E
E
E
E
E
E
E
E
E
Time
Temperature
E: Exception P: Previous
E

## Slide 34: Exception Test - Results
Time
Temperature
Successive values sent to the PI Data Archive.
When a value is sent, it becomes the new snapshot.

## Slide 35: Storing Only Meaningful Data

## Slide 36: Compression Test – Example
Time
Temperature
A: Archived Value
A
A
A
A
A
A
A
The compression algorithm is performed on new snapshots to determine which data is kept in the PI archives.

## Slide 37: Compression Results
Time
Temperature
When the user requests a tag-time for which the value is interpolated, the difference can be no greater than ±CompDev.
Values kept in the PI archives.

## Slide 38: Compression Results
Raw values scanned.
..After Compression.
.After Exception.
Temperature
Time

## Slide 39: Valid PI time expressions
Only a Fixed time
Only a Reference-time abbreviation
Only a Time Offset
A combination of Fixed time or Reference-time abbreviation with a Time Offset
25-Jul-2013 11:00:00 AM
*
+8h
t+8h

## Slide 40: Fixed Time
A fixed time always represents the same time, regardless of the current time.
Input | Meaning
25-Jul-2013 11:00:00 AM | 11:00 AM on July 25, 2013
8-Apr-2013 | Midnight (00:00:00) on April 8, 2013
10/7/2013 4:00:00 PM | 4 PM on October 7, 2013.
This is the PI Time format. PI Clients will interpret it correctly regardless of the computer regional settings.
This is the time format for English (United States).

## Slide 41: Relative time
Abbreviations can be used in the PI System to represent a time that is relative to the current time.
Today at midnight
Yesterday at midnight
Now
Most popular abbreviations
Tuesday at midnight (most recent Tuesday)
Current month and day in the year 2011 (at midnight)
25th day of the current month at midnight
First day of the current month at midnight
Other abbreviations

## Slide 42: Time-unit Abbreviations
Time +/- number of units
  Hours (h)
  Minutes (m)
  Seconds (s)
  Weeks (w)
  Days (d)
  Years (y)
  Months (mo)

## Slide 43: Times with an Offset
Add or subtract a time to a fixed or relative time:
Input | Meaning
*-1h | One hour ago
t+8h | 08:00:00 (8:00 a.m.) today
y-8h | 16:00:00 (4:00 p.m.) the day before yesterday
mon+14.5h | 14:30:00 (2:30 p.m.) last Monday
sat-1m | 23:59:00 (11:59 p.m.) last Friday
1-jan-11-1d | 00:00:00 (12:00 a.m.) 31 December 2010

## Slide 44: Lehigh PI System
PI Data Archive: pi-data.ad.lehigh.edu
Asset Framework (AF) Server: pi-data.ad.lehigh.edu
Coresight: pi-core.ad.lehigh.edu
  https://pi-core.ad.lehigh.edu/Coresight
If you wish to play around with other client tools, go to:
  http://software.lehigh.edu
  PI Visualization Tools

## Slide 45: PI Coresight
PI Coresight is the fastest and easiest way to visualize PI System Data

## Slide 46: PI Coresight Displays
Create a new display
Explain the Search mechanism and the data symbols included in the search
Identify the various icons related to the search results
List the dynamic symbols available

## Slide 47: PI WebAPI
REST based API
Cross platform, supports multiple users, easy to deploy
  Good for web/mobile applications
PI Indexed Search
  Default Feature
  Creates indices for the PI and AF Databases to allow for faster searches

## Slide 48: PI WebAPI Live Demo
We will be using Internet Explorer to browse the website
  Any web browser will do
We will be using Postman – Chrome add-in
  Can use any API Development tool
  Can use a web debugging tool like Fiddler
Additional Resources:
  https://techsupport.osisoft.com/Troubleshooting/KB/KB01128

## Slide 49: PI WebAPI WebPage
Link to Library of functions and Getting Started Guide
PI WebAPI Queries
(Http Get requests)

## Slide 50: HTTP Requests
Use HTTP verbs to specify the “type” of request
  POST, GET, PUT or PATCH, Delete
  Create, Read, Update, Delete
We can see what type the request is using developer tools on web browser (F12)

## Slide 51: Lets try to Connect to the WebAPI Site
Authorization error: This is because WebAPI some form of authorization to access
  At Lehigh we will be using basic authentication

## Slide 52: Let’s add in Basic Authentication
Postman has a built in Base64 encoder
  If you are using a different program, you’ll need to encode your credentials
Syntax:
  Authentication: Basic Base64 encoding of user credentials
  Ex: Authorization: Basic YWRceDAwZjE2Ok9zaXNvZnQjMQ==

## Slide 53: Let’s Search for Some Tags
When starting out, always refer to the WebAPI help page
For the purposes of the Hackathon, we will be trying to access data from the Williams building
  All tags that were created for the Williams building will start with BACnet Connector

## Slide 54: Let’s Try Querying for a PI Tag
PI Tags are organized as: \\PI-DataArchive\PITagName
Remember Spaces are not allowed for URLS. Space=%20

## Slide 55: With a PI Tag, we can get data
Let’s first get the latest data point (as Osisoft calls it: event)

## Slide 56: With a PI Tag, we can also get an event in the past
Now let’s get a data point for the past. This time we will need to specify a timestamp.
Time is represented using the PI Time Format.
Input time will be your local time BUT
All time values the return query is in UTC time (4 hours ahead)

## Slide 57: With a PI Tag, we can also get an event in the past
Now let’s get a data point for the past. This time we will need to specify a timestamp.
Time is represented using the PI Time Format.
Input time will be your local time BUT
All time values the return query is in UTC time (4 hours ahead)

## Slide 58: Lets make our queries more efficient
We can also query for all events over a time range

## Slide 59: Use webAPI we can also write data to PI Server too
As mentioned earlier, one of the key sources of data is using connectors.
  We will be using the UFL Connector
We will be connecting to a REST endpoint to post data to tags.
  https://pi-node.ad.Lehigh.edu:5460/connectordata/Student%20Qualcomm/
  You will be able to connect using Basic Authentication
    Username: LehighHacks
    Password: LU!H@cks

## Slide 60: Thanks!